## Slide 1: ARROW: Restoration-Aware Traffic Engineering
Zhizhen Zhong
MIT CSAIL
Manya Ghobadi
Alaa Khaddaj
Jonathan Leach
Yiting Xia
Ying Zhang

## Slide 2: Wide-Area Networks (WANs)
The workhorses of today’s global Internet services.
Billion-dollar assets.
Must be efficiently utilized.
Fiber optic cables
Level3 global backbone

## Slide 3
Gain 2x throughput without compromising availability
in large-scale WANs.
This talk: ARROW

## Slide 4: Talk outline
Opportunity
System
Evaluations
State-of-the-art
Failed IP links can be restored.
Dynamically restore failed IP links with ARROW.
Impact of fiber cuts on WANs.
Gains of restoration-aware WANs

## Slide 5: What is a WAN link?
Router
Router
IP link
Fiber
5
Boston
San Francisco
Optical switch
Optical switch
Transponder
Transponder
Router
Router
Optical wavelength (λ)
Amplifier

## Slide 6: WAN’s IP/optical topology mapping
6
WAN operators’ goal
Maximizing network throughput while maintaining high availability.
IP layer
Optical layer
B
C
A
D
A
B
C
D

## Slide 7: Problem: fiber cuts are common at large scale
http://users.ece.utexas.edu/~kwasinski/ikegrid.html
https://www.kfyrtv.com/content/news/Cut-cables-in-Minot-leads-to-Internet-outage-570098031.html
https://www.youtube.com/watch?v=VVJlKJi9FWU

## Slide 8: Fiber cuts take down several Tbps IP capacity
Chart: Lost capacity (Tbps)
9/2017 12/2017 3/2018 6/2018 9/2018
Chart: 
| 1518390779 | 1518390780 | 1518391110 | 1518391111
Y-Values | 0 | 7.4 | 7.4 | 0
9 am 6pm
9 hours

## Slide 9: State-of-the-art approach to cope with fiber cuts
IP1
Backup IP1
λ1
Backup λ1
IP layer
Optical layer
B
C
A
D
A
B
C
D
λ2
Backup λ2
IP2
Backup IP2
State-of-the-art approach
Needs backup link to maintain availability.
Requires extra router ports & transponders for backup links.

## Slide 10: Talk outline
Opportunity
System
Evaluations
State-of-the-art
Failed IP links can be restored.
Dynamically restore failed IP links with ARROW.
Impact of fiber cuts on WANs.
Gains of restoration-aware WANs.

## Slide 11: ARROW: Agile Restorable Optical Wavelengths
IP layer
Optical layer
IP1
Restored IP1
λ1
Restored λ1
B
C
A
D
A
B
C
D
λ2
Restored λ2
IP2
Restored IP2
Key idea in ARROW
Reconfiguring wavelengths to restore lost IP capacity.
No redundant router ports or transponders.
11

## Slide 12: How to plan IP/optical restoration?
Feed into traffic engineering optimization.
Iterate over all plausible fiber cut scenarios on the optical layer.
Decide on restoration plan for each fiber cut scenario.
[Optical layer]
[IP layer]

## Slide 13: Is there enough room in the optical fibers?
Fiber restoration ratio (%)
Chart: CDF
62% of fibers are partially restorable

## Slide 14: Challenge: partial restoration
Optical-layer network
B
C
A
D
4
8
Full restoration
Partial restoration
8
4
B
C
A
D
3 free wavelengths
2 free wavelengths
1
3
B
C
A
D
1
1
1
B
C
A
D
1
2
1
2
B
C
A
D
1
1
1
B
C
A
D
2
2
Many partial restoration candidates with the same restored capacity!

## Slide 15: Example of partial restoration challenge
A
B
C
D
A
B
C
D
A
B
C
D
IP layer
Healthy state
Total restored capacity: 5
1
1
1
2
3
1
1
Total restored capacity: 5
3 free wavelengths
2 free wavelengths
B
C
A
D
4
8
B
C
A
D
B
C
A
D
Optical layer
Throughput = 500 Gbps
Throughput = 300 Gbps
Throughput = 500 Gbps
Demand: 400 Gbps
Demand: 100 Gbps
Satisfied demand: 200 Gbps
Satisfied demand: 100 Gbps
Satisfied demand: 400 Gbps
Satisfied demand: 100 Gbps
Restoration candidate 1
Restoration candidate 2

## Slide 16: Handling partial restoration
Which partial restoration candidate leads to the best network throughput?
Devise a novel LotteryTickets abstraction to augment IP-layer traffic engineering with optical-layer restoration awareness.
Question
ARROW’s approach

## Slide 17: Talk outline
Opportunity
System
Evaluation
State-of-the-art
Failed IP links can be restored.
Dynamically restore failed IP links with ARROW.
Impact of fiber cuts on WANs.
Gains of restoration-aware WANs.

## Slide 18: Ideal solution: cross-layer IP/optical traffic engineering
Traffic demand
IP topology
IP layer
Optical layer
Optical topology
Set of failure scenarios
Integer-linear program (ILP)
Billions of variables for today’s WANs! Computationally intractable.
Traffic splitting ratio
Restoration plan
Cross-layer formulation
…

## Slide 19: Root causes for computational intractability
IP and optical layers are orthogonal in problem space.
Mapping between IP links and their corresponding wavelengths is binary.
Optical layer constraints
IP layer constraints
Problem space

## Slide 20: ARROW’s key technique: LotteryTicket abstraction
Solve the optical layer integer problem offline, and record solutions (failed IP links’ restorable capacity) as LotteryTickets.
Only feed LotteryTickets into IP-layer traffic engineering.
Optical layer constraints
IP layer constraints
Problem space
Offline solve
Solutions as LotteryTickets

## Slide 21
Traffic demand
IP topology
IP layer
Optical layer
Optical topology
Set of failure scenarios
Traffic splitting ratio
Restoration plan
Cross-layer formulation
ARROW traffic engineering system
Offline calculated with Randomized Rounding
Restoration candidates
Lottery Tickets
ARROW’s formulation
Linear program (LP)
Fast runtime on today’s WANs.
…

## Slide 22: Handling wavelength reconfiguration
Can the optical hardware support fast wavelengths reconfiguration?
Amplifiers add several minutes of delay when reconfiguring wavelengths.
Question
Decades-old challenge
Use noise to avoid amplifier adjustments by fully populating the fibers.
ARROW’s approach

## Slide 23: How fast can we reconfigure wavelengths?
Bottom fiber’s active wavelength number changed (λ1 -> λ1+λ2)
Bottom fiber’s amplifiers adjustment required
Amplifier adjustments takes minutes
failure
λ2
λ1
Amplifier
Optical switch
A
Optical switch
B
Reconfigured λ1
Power
𝜆1
Wavelength frequency on top fiber
Power
𝜆2
Wavelength frequency on bottom fiber
𝜆1

## Slide 24: Noise loading bypasses amplifier adjustments
Amplifier
Bottom fiber’s active wavelength number (λ1+λ2) is constant
No adjustments to amplifiers
Optical switch
A
Optical switch
B
failure
λ2 data
λ1 data
λ1 carrying noise
λ1 data
Noise source
Noise source
Amplifier adjustment delay can be saved
Power
𝜆1
Wavelength frequency on Fiber1
Power
𝜆2
Wavelength frequency on Fiber2
𝜆1 carrying noise
𝜆1

## Slide 25: Talk outline
Opportunity
System
Evaluation
State-of-the-art
Failed IP links can be restored.
Dynamically restore failed IP links with ARROW.
Impact of fiber cuts on WANs.
Gains of restoration-aware WANs.

## Slide 26: Production testbed
D
B
A
C
360 km
140 km
200 km
180 km
Amplifier (EDFA)
Transponders
D
B
A
C
Optical Transponders
2160 km fiber
Optical switch
Amplifiers

## Slide 27: A fiber cut restoration trial
(a) Healthy network
Router B
Router A
Router D
Router C
(c) Restored network
λ9 – λ14
Router B
Router A
Router D
Router C
(b) Network under fiber cut
Router B
Router A
Router D
Router C
D
B
A
C
IP layer
Optical layer
D
B
A
C
D
B
A
C
λ1 – λ2
failure
failure
λ9 – λ14
λ15 – λ16
λ3 – λ8
λ1 – λ2
λ9 – λ14
λ15 – λ16
λ3 – λ8
λ1 – λ2
λ9 – λ14
λ15 – λ16
λ3 – λ8
Reconfiguring 14 wavelengths:
17 minutes (State-of-the-art) -> 8 seconds (ARROW).

## Slide 28: Simulation setup
Topology |  |  |  |  | Traffic matrix | Tunnel selection | Baseline TE algorithms
Name | # routers | # IP links | # optical switches | # fibers |  |  | 
B4 | 12 | 52 | 12 | 19 | Traffic trace from SMORE [NSDI’18] | Fiber-disjoint paths & k-shortest paths | FFC [SIGCOMM’14] ECMP [TON’16] TeaVaR [SIGCOMM’19]
IBM | 17 | 85 | 17 | 23 |  |  | 
Facebook | 34 | 262 | 84 | 156 | production traffic trace (sample every 30 minutes) |  | 

## Slide 29: Simulation results: availability
Chart: Demand Scale
| 0.99999999999999989 | 1.3333333333333333 | 1.6666666666666665 | 1.9999999999999998 | 2.333333333333333 | 2.6666666666666665 | 3 | 3.333333333333333 | 3.666666666666667 | 3.9999999999999996 | 4.3333333333333339 | 4.6666666666666661 | 5 | 5.333333333333333 | 5.6666666666666661 | 6 | 6.333333333333333 | 6.6666666666666661
FFC-2 | 100 | 99.998 | 99.9823 | 99.9361 | 99.8024 | 99.502 | 98.9959 | 98.2188 | 97.2608 | 96.0428 | 94.664 | 93.2231 | 91.6713 | 90.0212 | 88.3675 | 86.6079 | 84.853 | 83.118
TeaVaR | 100 | 99.9982 | 99.9833 | 99.9393 | 99.8148 | 99.6276 | 99.322 | 98.8414 | 98.5812 | 98.0846 | 97.6295 | 96.93 | 96.3838 | 95.7767 | 94.7293 | 94.2751 | 93.1815 | 92.3909
ECMP | 100 | 99.9984 | 99.984 | 99.9419 | 99.8177 | 99.5301 | 99.0289 | 98.2459 | 97.2461 | 95.9635 | 94.4905 | 92.9461 | 91.259 | 89.552 | 87.7682 | 85.9078 | 84.1018 | 82.3804
ARROW | 100 | 100 | 100 | 100 | 99.9999 | 99.9995 | 99.9978 | 99.9945 | 99.9892 | 99.9814 | 99.9626 | 99.9352 | 99.8455 | 99.5543 | 99.4028 | 99.1326 | 98.584 | 98.2157
ArrowNaive | 100 | 100 | 100 | 99.9804 | 99.9267 | 99.7749 | 99.595 | 99.1647 | 98.735 | 98.1751 | 97.7184 | 96.7751 | 96.1373 | 95.5347 | 94.7702 | 94.1876 | 93.4839 | 92.8262
ECMP
ARROW
[SIGCOMM’14]
[SIGCOMM’19]
better
99.9%
2x more traffic
FFC
TeaVaR
[TON’16]
By reconfiguring wavelengths to restore failed IP links, we carry 2x more traffic while maintaining a highly available network.
ARROW (1 LotteryTicket)
(80 LotteryTickets)

## Slide 30: Simulation results: throughput
Chart: # of LotteryTickets
ARROW (1 LotteryTicket)

## Slide 31: Concluding summary
ARROW is a traffic engineering system that reconfigures wavelengths during fiber cuts.
Our LotteryTicket abstraction makes cross-layer traffic engineering feasible at large scale to meet the stringent TE runtime requirement.
ARROW supports 2x – 2.4x more network throughput without compromising availability.
Code available at http://arrow.csail.mit.edu.